## Slide 1
Introduction
to
Microprocessors
Course ID: CSE - 341
Course Title: Microprocessors
Course Teacher: Md. Motaharul Islam, PhD
Associate Professor Department of Computer Science & Engineering BRAC University.

## Slide 2: Topics to be Covered in this Course !!
Microprocessor and Assembly Language:
Microprocessors and Microcomputers
Evaluation of Microprocessors Applications
Intel 8086 Microprocessor: internal architecture, register structure, programming model, addressing modes, instruction set
Assembly language programming
Coprocessors.
An overview of Intel 80186, 80286, 80386, 80486 and Pentium microprocessors
RISC and CISC processors.

## Slide 3: Recommended Texts
Microprocessors and Interfacing: Programming and Hardware, Author: Douglas V. Hall
Assembly Language Programming and Organization of the IBM PC, Author: Ytha Yu, Charles Marut
Microprocessor, architecture, programming & application with the 8085, Author: Gaonkar
The Intel Microprocessor 8086…Arch. Prog, Interfacing. Author: Bary, Bray
  Microprocessor and Microcomputer – Based System Design, Author: Mohamed Rafiquzzaman

## Slide 4: Does Earlier Knowledge Require ??
You should have the knowledge about –
  Number Systems.
  Basics of “Digital Logic Design” course.
  Basics of “Computer Organization and Architecture” course.
  “Basic Programming”.

## Slide 5: Concept of Computer
Computer
Data Processing
Data Storage

## Slide 6: Major Components of Computer
Computer
CPU
MEMORY
I/O
SYSTEM BUS

## Slide 7: Concept about Microprocessor
A microprocessor incorporates most or all of the functions of a central processing unit (CPU) on a single integrated circuit (IC).
CPU
Die of an Intel 80486DX2 microprocessor (actual size: 12×6.75 mm) in its packaging

## Slide 8: Central Processing Unit
A central processing unit (CPU), or sometimes just called Microprocessor (P), is a description of a class of logic machines that can execute computer programs.
This broad definition can easily be applied to many early computers that existed long before the term "CPU" ever came into widespread usage. However, the term itself and its initialism have been in use in the computer industry at least since the early 1960s.
The form, design and implementation of CPUs have changed dramatically since the earliest examples, but their fundamental operation has remained much the same.

## Slide 9: Central Processing Unit/Microprocessor (P)
Control Unit & Instruction Decoder
Arithmetic/Logic Unit
Registers
To decode instruction and
pass the necessary control signals to CU
To synchronize and control the
overall operation of the P system
    To perform the arithmetic and logical
    operations within the CPU
To perform shift and rotate
operations that may either be
arithmetic or logical in nature
Control and Status Registers
User-Variable Registers
A set of internal storage
locations within the CPU

## Slide 10: So .. What is Microprocessor?
A microprocessor (abbreviated as µP or uP) is a Silicon Chip that contains an electronic central processing unit (CPU). In the world uP or CPU used interchangeably, which is made from miniaturized transistors and other circuit elements on a single semiconductor integrated circuit (IC).
The integration of the whole CPU onto a single VLSI Chip therefore greatly reduced the cost of processing capacity.
Architectures of Microprocessors:
  8-bit designs
  16-bit designs
  32-bit designs
  64-bit designs
  Multi-core designs
  RISC (Reduced Instruction Set Computer)
  CISC (Complex Instruction Set Computer)
  Special-purpose designs: Microcontrollers, Digital Signal Processors (DSP) and Graphics Processing Units (GPU).

## Slide 11: List of Microprocessors
1971 - Intel 4004, 1st single chip CPU, 4-bit processor, 45 instructions
1972 - Intel 4040, enhanced 4004, 60 instructions
1972 - Intel 8008, 8-bit P
1972 - Texas Instrument TMS 1000, 1st single C, 4-bit
1974 - Intel 8080, successor to the 8008, used in Altair 8800
1975 - Motorola 6800, used MOS technology
1976 - Intel 8085, updated 8080, +5V power supply
1976 - Zilog Z80, improved 8080
1976 - TI TMS 9900, 1st 16-bit P
1978 - Zilog Z8000, Motorola 68000, 16-bit P
1978 - Intel 8086, 16-bit, IBM’s choice...

## Slide 12: Similar but Different !! Microcontroller (C)
Microcontroller is an IC dedicated to perform one task.
  Integrates the memory and other features of a microprocessor.
  A microcontroller is the integration of
    Microprocessor
    Memory
      ROM types – commonly flash PROM
      RAM – Static ram
CPU
MEMORY
I/O
SYSTEM BUS

## Slide 13: List of Microcontrollers
1972 - Texas Instrument TMS 1000, 1st single C, 4-bit
1976 - Intel 8048, 8-bit C, 1k ROM, 64b RAM, 27 I/O
1980 - Intel 8051, 4k ROM, 128b RAM, 32 I/O, 2 16-bits timers
1980s
(MCS-51 family)
- Intel 8031, 8052, 8751, …
- Atmel AT89C51, AT 89C1052/2051,…
- Dallas Semiconductor DS5000 series…
Philips, National Semiconductor, …
(Other Cs) Microchip PIC16 series, Motorola 68HC11, Zilog’s Z86

## Slide 14: Microprocessor System Vs Microcontroller System

## Slide 15: Microprocessor System Vs Microcontroller System
CPU
General
purpose
Micro
processor
Data Bus
Address Bus
RAM
ROM
I / O
Port
Timer
Serial
COM
Port
CPU
RAM
ROM
I / O
Port
Timer
Serial
COM
Port
General-Purpose Microprocessor System
Microcontroller

## Slide 16: Assembly Language
Assembly language:
  Assembly language is used for most programming because it is difficult to program a microprocessor in its native, that is hexadecimal machine language.
Assembler:
  An assembler is a program that converts software written in symbolic machine language (the source programme) into hexadecimal machine language (object programme).
  The primary reason to use assembler is because development and modification are always difficult in machine language.

## Slide 17: Example of 8085 Assembly Language
Address Instruction
202A MVI A, 21H ; Copies 21 into accumulator
202C MVI B, 2AH ; Copies 2A into B register
202E ADD B ; Adds B reg. content with Acc and stores the result in Acc.
202F STA [41 FF] ; Stores the Acc (the sum) into the memory location 41 FF.
2032 HLT ; Stops the program

## Slide 18: Memory storage of the Assembly language
Address Instruction/Data
202A MVI A,
202B 21
202C MVI B,
202D 2A
202E ADD B
202F STA
2030 FF
41
2032 HLT

## Slide 19: Another Example of 8085 Assembly Language
Address Instruction
2020 MVI B, 24 ; Copies 24 into B register
2022 INR B ; Increment B reg content by 1
2023 MOV A, B ; Copies B register into Acc.
2024 SUB B ; Subtracts B reg content from Acc and stores the result in Acc.
2025 STA [5F FF] ; Stores the Acc content into the memory location 5F FF.
2028 HLT ; Stops the program

## Slide 20: Assembly Language vs. Machine Language

## Slide 21: Thank You !!